Specification

Dimensions

- Dimensions: 115.5 x 58.1 x 13.6 mm

- Weight (with battery): 114 g

- Volume: 63.2 cc

Display and user interface

- Size: 2.4"

- Resolution: 320 x 240 pixels (TFT)

- 262,000 colours

- Landscape QVGA

Keys and input methods

- QWERTY keyboard

- Dedicated messaging and contacts keys

Colours

- Available colours:

  - Slate Grey

  - Hot Pink

  - Golden White

Colour selection is dependent on sale region.

Personalisation

- Customisable home screen:

  - widgets

  - themes

  - shortcuts

- Ringtones: AAC, eAAC+, MP3, WMA, MIDI

- Video ringtones

- Themes

  - wallpapers

  - ringtones

  - pre-installed themes

## Hardware

Power Management

- BL-5J 1320 mAh Li-Ion battery

- Talk time (maximum):

  - up to 7 hours

- Standby time (maximum):

  - up to 800 hours

- Music playback time (offline mode, maximum): 30 hours

Operation times may vary depending on radio access technology used, operator network configuration and usage.

Memory

- MicroSD memory card slot, hot swappable, up to 8 GB

- Internal memory: 55 MB

Operating frequency

- Quad band EGSM 850/900/1800/1900

- Automatic switching between GSM bands

- Flight mode

Data network

- GPRS class A, multislot class 32, maximum speed 85.6/64.2 kbps (DL/UL)

- EGPRS class A, multislot class 32, maximum speed 296/177,6 kbps (DL/UL)

- WLAN IEEE 802.11b/g, maximum speed up to 11 Mbps/54 Mbps

- TCP/IP support

- Capability to serve as data modem

Requires data service. Data Services may not be available in all networks. Data transmission speeds may be as high as 236.8 kbps, but may vary based upon network capabilities and other conditions. The establishment and continuation of a data connection depends on network availability, provider support and signal strength.

Connectivity

- 2.0 mm Charger Connector

- Bluetooth version 2.1 with Enhanced Data Rate

- Support for local synchronisation

- High-Speed USB 2.0 (micro USB connector)

- 3.5 mm AV connector

## Software & Applications

Software platform & user interface

- Series 40

- FOTA (firmware update over the air)

- Software updates through Nokia Software Updater installed on PC

Applications

- Nokia Messaging Service 3.0 for Email

- Nokia Messaging Service 3.0 Chat

- Nokia Messaging Service 3.0 Communities

Personal Information Management (PIM)

- Detailed contact information

- Calendar

- To-do list

- Notes

- Recorder

- Calculator

- Clock

- Converter

## Communications

Email and messaging

- Easy access to your email accounts, including Yahoo!® Mail, Gmail™, Windows Live™, Hotmail™ and other popular POP/IMAP services

- Easy Ovi Mail free email account creation directly from phone

- Instant messaging through Windows Live Messenger™, Yahoo!® Messenger, Google Talk™ and Ovi Chat

- Conversational SMS for chat-style text messages

- SMS, MMS

- Nokia Xpress audio messaging

Call management

- Contacts: up to 1,000 entries

- Speed dialling

- Logs of dialled, received and missed calls

## Sharing & Internet

Browsing and internet

- Web browsing of real web pages through Nokia OSS web browser

- JavaScript version 1.3 and 1.5

- ECMAScript support

- CSS support

- OMA DRM version 2.0

- Supported mark-up languages: HTML, XHTML, WML

- Supported protocols: HTTP, WAP

- TCP/IP support

- Included Opera Mini browser optimises web page rending for mobile devices

- Web Search

- Communities widget on home screen shows live feeds from Facebook and Twitter

## Photography

Camera

- 2 megapixel camera (1600 x 1200 pixels)

- Still image formats: JPEG

- Zoom up to 4x (digital)

- Fullscreen viewfinder

- Self timer

- Effects in viewfinder: greyscale, sepia and negative

Other

- 55 MB internal memory, expandable to up to 8 GB with microSD card

- High-speed USB 2.0 connectivity

- Bluetooth 2.1 EDR wireless connectivity

## Video

Video camera

- 2 megapixel

- Video clip length: up to capacity of memory card

- Settings for scene, video light, white balance, colour tone

- Zoom up to 4 x digital

Video codecs & formats

- Video capture in MPEG-4, QCIF max. resolution 320 x 240

- Video file format: H.263, H.264, AVI, MPEG-4 (stored as .mpg or .3gp files), WMV

Video sharing and playback

- Support for download and streaming

## Music & audio

Music features

- Nokia Ovi Player

- Music codecs: .MP3, WMA, AAC, eAAC, eAAC+

- 3.5 mm stereo headphone plug

- Ringtones: mp3, aac, 64-tone polyphonic

Radio

- Stereo FM radio (87.5-108 MHz/76-90 MHz), RDS

## Gaming

Gaming

- Included games

  - Bounce

  - Sudoku

  - Block'd

  - Diamond Rush

Availability of games dependent upon sales region.

## Environmental features

Energy efficiency

- Unplug charger reminder

Eco content and services

- Available at Ovi, preinstalled eco wallpapers

Materials

- Free of PVC, free of nickel on the product surface, free of brominated & chlorinated compounds and free of antimony trioxide as defined in Nokia Substance List

Recycling

- All materials of the device can be recovered as materials and energy

Packaging

- Made of renewable, up to 57 % recycled material. 100 % recyclable, reduced flat package size

User guide

- Black & white printing, eco tips on Green Page

## Package contents

Standard Sales Package

- Nokia C3

- Nokia Battery BL-5J

- Nokia Compact Charger AC-3

- Nokia Stereo Headset WH-102

- Nokia 2 GB microSD Card MU-37

- User guide

## Accessories

Recommended accessories

- Nokia Bluetooth Headset BH-105

- Nokia 8 GB micro SDHC Card MU-43

Compatible mobile accessories Using Nokia or other consumer internet services with your mobile device may involve transferring large amounts of data. Your service provider may charge for the data transmission. The availability of particular products, services, and features may vary by region. Please check with your local Nokia dealer for further details and availability of language options. These specifications are subject to change without notice.

SAR Eco profile Declaration of conformity